## Slide 1: Solar Tracker
Presented by: Aditya Singh

## Slide 2: Abstract
This project focuses on maximizing solar energy efficiency using a dual-axis solar tracker integrated with IoT capabilities.
The ESP32 microcontroller controls servo motors based on LDR sensor readings to align the solar panel with the sun. Real-time data such as light intensity, voltage, and current are sent to the
ThingSpeak cloud for remote monitoring and analysis. The system increases energy generation efficiency by approximately 25–30% compared to fixed panels.

## Slide 3: Objectives
Maximize solar energy output by automatic tracking
Implement IoT-based remote monitoring and data logging
Analyze power generation performance over time

## Slide 4: Block Diagram (Concept)
LDR sensors detect sunlight intensity from four directions
ESP32 processes sensor data and controls two servo motors for panel movement
Voltage and current sensors measure panel output
Data sent to ThingSpeak via Wi-Fi for visualization
Components: ESP32, LDRs, Servo Motors, ACS712, Voltage Sensor, Solar Panel, ThingSpeak Cloud

## Slide 5: Hardware Components
1. ESP32 Microcontroller – core control and Wi-Fi communication
2. LDR Sensors – sunlight detection
3. Servo Motors (2x) – dual-axis panel adjustment
4. ACS712 Current Sensor – power measurement
5. Voltage Sensor – voltage monitoring
6. Solar Panel – energy source
7. Power Supply (5V/12V) – system power
8. ThingSpeak Cloud – IoT data visualization

## Slide 6: Working Principle
1. LDRs sense sunlight intensity and send data to ESP32.
2. ESP32 calculates intensity difference and moves servos to align panel.
3. Voltage and current sensors measure panel output.
4. ESP32 sends light, voltage, and current data to ThingSpeak.
5. Cloud dashboard displays real-time graphs for monitoring.

## Slide 7: Results and Discussion
The tracker maintains perpendicular orientation to sunlight.
Improved power generation efficiency (~25–30%).
Stable ThingSpeak data visualization and monitoring.
Reliable performance under varying weather conditions.

## Slide 8: Advantages
Increased energy efficiency
Remote monitoring via IoT

## Slide 9: Conclusion
The IoT-based dual-axis solar tracker using ESP32 successfully integrates renewable energy tracking with modern IoT capabilities. By maintaining optimal solar alignment and providing real-time monitoring through ThingSpeak, the system demonstrates increased efficiency and smarter energy management.