## Slide 1
Solar Tracker
A Smart Renewable Energy Monitoring System
Presented by: Aditya Singh
Notes: 1

## Slide 2
Abstract / Overview
- This project focuses on maximizing solar energy efficiency using a dual-axis solar tracker integrated with IoT capabilities. The ESP32 microcontroller controls servo motors based on LDR sensor readings to align the solar panel with the sun. Real-time data such as light intensity, voltage, and current are sent to the ThingSpeak cloud for remote monitoring and analysis. The system increases energy generation efficiency by approximately 25–30% compared to fixed panels.
Notes: 2

## Slide 3
Objectives
• Maximize solar energy output by automatic tracking
• Implement IoT-based remote monitoring and data logging
• Analyze power generation performance over time
• Reduce manual intervention and maintenance efforts
Notes: 3

## Slide 4
Block Diagram (Concept)
• LDR sensors detect sunlight intensity from four directions
• ESP32 processes sensor data and controls two servo motors for panel movement
• Voltage and current sensors measure panel output
• Data sent to ThingSpeak via Wi-Fi for visualization
• Components: ESP32, LDRs, Servo Motors, ACS712, Voltage Sensor, Solar Panel, ThingSpeak Cloud
Notes: 4

## Slide 5
Hardware Components
1. ESP32 Microcontroller – core control and Wi-Fi communication
2. LDR Sensors – sunlight detection
3. Servo Motors (2x) – dual-axis panel adjustment
4. ACS712 Current Sensor – power measurement
5. Voltage Sensor – voltage monitoring
6. Solar Panel – energy source
7. Power Supply (5V/12V) – system power
8. ThingSpeak Cloud – IoT data visualization
Notes: 5

## Slide 6
Working Principle
1. LDRs sense sunlight intensity and send data to ESP32.
2. ESP32 calculates intensity difference and moves servos to align panel.
3. Voltage and current sensors measure panel output.
4. ESP32 sends light, voltage, and current data to ThingSpeak.
5. Cloud dashboard displays real-time graphs for monitoring.
Notes: 6

## Slide 7
IoT Implementation
• IoT Platform: ThingSpeak
• Data sent: Light Intensity, Voltage, Current, Power (P=V×I)
• Communication: Wi-Fi using HTTP API
• Visualization: Real-time graphs and analysis on ThingSpeak dashboard
• Benefit: Remote monitoring and performance comparison
Notes: 7

## Slide 8
Results and Discussion
• The tracker maintains perpendicular orientation to sunlight.
• Improved power generation efficiency (~25–30%).
• Stable ThingSpeak data visualization and monitoring.
• Reliable performance under varying weather conditions.
Notes: 8

## Slide 9
Advantages & Future Scope
- Advantages:
- • Increased energy efficiency
- • Remote monitoring via IoT
- • Reduced manual adjustment
- Future Enhancements:
- • Predictive tracking using solar angle algorithms
- • GSM/Lora connectivity for rural deployment
- • Machine Learning-based optimization
- • Automatic cleaning or fault detection systems
Notes: 9

## Slide 10
Conclusion
- The IoT-based dual-axis solar tracker using ESP32 successfully integrates renewable energy tracking with modern IoT capabilities. By maintaining optimal solar alignment and providing real-time monitoring through ThingSpeak, the system demonstrates increased efficiency and smarter energy management.
Notes: 10